## Slide 1
Method for assessing 37Ar emissions from nuclear reactors
Martin Kalinowski1, Pouneh Tayyebi2
P3.5-483
1 CTBTO, IDC
2 Nuclear science and technology research institute (NSTRI), Tehran, Iran

## Slide 2
ABSTRACT
Method for assessing 37Ar emissions from nuclear reactors
Martin Kalinowski, Pouneh Tayyebi
37Ar is an indicator of an underground nuclear explosion. This radioisotope is produced via 40Ca (n, α) 37Ar reaction through neutron activation of 40Ca included in the rocks near to the nuclear explosion location. The relatively long half-life of 35 days compared to CTBT-relevant radioxenon isotopes results into 37Ar activity becoming stronger than radioxenon activity approximately 50 days after detonation. Normal operational releases of 37Ar from nuclear facilities contributes to the atmospheric background. It can be produced via neutron activation of air or of gas dissolved in water. The emissions of this isotope are not regularly measured and very few release data are available. Therefore, the two-step method presented here is more complex than the method the authors had applied previously for assessing 37Ar releases from nuclear research reactors. As the first step, simulations with ORIGEN determine isotopic ratios of 37Ar and an appropriate proxy like 41Ar for which stack release data are available. These ratios are depending on the duration of the irradiation and the intensity of the neutron flux. As second step, the retention time is used to account for the decay between escaping the neutron flux and getting released through the stack.
P3.5-483

## Slide 3
INTRODUCTION
Method for assessing 37Ar emissions from nuclear reactors
Martin Kalinowski, Pouneh Tayyebi
Klingberg et al. (2013) showed that radioxenon, including non-traditional radioxenon isotopes, resulting from activation in the HFIR research reactor could be observed at IMS stations.
Kirchner et al. (2020) identified the process resulting in the largest possible releases of 37Ar from NPPs being activation of 36Ar dissolved in the primary coolant. Under certain conditions it could be detected beyond 100 km from the emitting plant.
Such studies raise the question to what extend and under what conditions radioxenon resulting from activation could be observed at IMS stations.
The method suggested here for estimating 37Ar releases can be extended to radioxenon.
P3.5-483

## Slide 4
METHODS
Simple method used previously
Kalinowski/Tayyebi (2019) estimated the release of 37Ar of research reactors based on a scaling factor, SF, from the logarithmic mean of 37Ar release rates reported for a few NRRs:
SF = 111 Bq/kWh
The estimated annual emission from each nuclear research reactor is calculated with the following equation:
R = SF × CF × P × 365 × 24
Where
                R (Bq/y): release rate
                SF (Bq/kWh): Scaling factor
                CF: capacity factor
                P (kW): power
                365×24: converting factor for h/y
P3.5-483

## Slide 5
METHODS
Two step method
More robust method:
Here, we show a method for estimating the release of 37Ar using 41Ar as proxy because for this isotope stack release data are often available.
This works for all situations where activation in air or water is the main production path.
As first step, ORIGEN simulations were done to determine the activity ratio of 37Ar to 41Ar . We studied how these ratios are depending on the duration of the irradiation and the intensity of the neutron flux.
As second step, the retention time is used to account for the decay between escaping the neutron flux and getting released through the stack.
Resulting solution:
With the ORIGEN results of activity ratios at the end of irradiation and the decay correction using the retention time, the 37Ar release can be determined from 41Ar release reports.
P3.5-483

## Slide 6
METHODS
Method to determine irradiation and retention time
Differential equation for the activity of isotope i in the reactor:
A - Activity release rate
B - Birth rate from activation
      λ – Radioactive decay constant
      z – Effective retention time
In case of equilibrium, the ratio of birth rate and the release rates leads to this equation:
P3.5-483

## Slide 7
METHODS
Since both isotopes are the same gas (argon), we can assume z1=z2. The simplified equation can be solved for z and get possible retention times depending on the birth rate ratio calculated with ORIGEN, if reported releases are available:
This leaves still the question open what irradiation time can be assumed.
The idea is to find a match between irradiation time and retention time using additional information confining the technically reasonable ranges of these times.
Further confirmation of these times to reflect the reality well may come from results for other pairs of radioactive noble gas isotopes.
P3.5-483
Method to determine irradiation and retention time

## Slide 8
RESULTS
Saturation level of 37Ar / 41Ar
ORIGEN simulations were done for a typical NRR for a full year with a periodic cycle of 5 days irradiation and several 2 days cooling time.
The figure shows: the activity ratio of 37Ar to 41Ar reaches saturation after about 200 days.
The high variability results from the short half-life of 41Ar .
Radioisotope | Half life
37Ar | 35.04 d
41Ar | 109.34 m
P3.5-483

## Slide 9
RESULTS
The figure shows the activity ratio of 41Ar to 37Ar initially starts at very high levels that depend on the irradiation time.
This result is consistent with the ratio of 8430 as measured by Johnson et al. (2017) at the argon purge stack of the Texas TRIGA reactor.
Conclusion: Two parameters need to be known to use 41Ar as proxy for 37Ar :
      Irradiation time
      Retention time
P3.5-483
Saturation level of 37Ar / 41Ar

## Slide 10
RESULTS
ORIGEN simulations were done for 2 types of NPP (BWR and PWR) for a full year of constant power.
The figure shows the activity ratio of 37Ar to 41Ar reaches saturation after about 200 days, irrespective of NPP type.
P3.5-483
Saturation level of 37Ar / 41Ar

## Slide 11
RESULTS
Irradiation and retention time
Additional information to confine the possible range for the retention time: Kirchner et al. (2020) finds for 37Ar an exhaust air retention time of less than 24 hours.
The ORIGEN simulations show that the results are more critically dependent on the irradiation time. Therefore, we fix the retention time e.g. to 12 hours and find the matching irradiation time.
P3.5-483
 | ORIGEN2.1 |  |  | Johnson et al. (2017) |  | 
Z (h) | irradiation time (m) | estimated release ratio of 41Ar / 37Ar | estimated release 37Ar (mBq/m3) | release ratio of 41Ar / 37Ar | released 41Ar (mBq/m3) | released 37Ar (mBq/m3)
1 | 146 | 8.51E+03 | 1.20E+04 | 8.43E+03 | 1.02E+08 | 1.21E+04
2 | 65 | 8.37E+03 | 1.22E+04 |  |  | 
3 | 5 | 8.27E+03 | 1.23E+04 |  |  | 

## Slide 12
CONCLUSIONS
Method for assessing 37Ar emissions from nuclear reactors
Martin Kalinowski, Pouneh Tayyebi
Results of this work
37Ar is important as indicator of an underground nuclear explosion.
Reactor (NPP, NRR) emissions contribute to the ambient background and need to be assessed.
This presentation describes a method how to achieve this.
Outlook
The method needs to be validated against data. Initial checks are giving confidence.
Next, the method will be extended to predict radioxenon releases from activation.
The first application using a graphical trial and error approach is very promising.
See Tayyebi/Kalinowski at SnT2021, O3.5-456
P3.5-483

## Slide 13
Method for assessing 37Ar emissions from nuclear reactors
Martin Kalinowski, Pouneh Tayyebi
P3.5-483
References
Fay (2014), Characterization of Sources of Radioargon in a Research Reactor, The University of Texas at Austin.
Fay et al. (2013) Contributions to the 37Ar background by research reactor Operations, J Radioanal Nucl Chem, 296:273–277.
Johnson et al. (2017) Production and release rate of 37Ar from the UT TRIGA Mark-II research reactor, Journal of Environmental Radioactivity 167, 249-253.
Kalinowski/Tayyebi (2019) Investigation of emission of 37Ar from all nuclear research reactors worldwide. INGE2019 in Freiburg, Germany.
Kirchner et al. (2020). Will 37Ar emissions from light water power reactors become an obstacle to its use for nuclear explosion monitoring Journal of Environmental Radioactivity, 223, 106392.
Klingberg et al. (2013). Radioxenon signatures from activation of environmental xenon, Journal of Radioanalytical and Nuclear Chemistry, 296(1), 117-123.