## Slide 1
Statistical study of the Cs-137 detections at RN43 station
Mohamed Mahmoud Mounja1, Claudia Sanguigni2; Antonietta Rizzo2; Giuseppe Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy
O2.4-406

## Slide 2
O2.4-406
ABSTRACT
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
This work is the result of a joint collaboration between the Italian and the Mauritanian National Data Centers.
The historical analysis of the occurrence of relevant radionuclides at RN43 over the past ten years showed that the main contributor was Cs-137, causing several level 3 and level 4.
A descriptive statistical analysis of the Cs-137 occurrence was performed and two types of parametric process control methods were applied: the “Shewhart Control Chart” and the “Exponentially Weighted Moving Average (EWMA) Control Chart”.
The results of both methods were then analyzed in order to reveal seasonality, possible sources of Cs-137 and correlation with atmospheric phenomena.

## Slide 3
INTRODUCTION
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406

## Slide 4
Chart: Aerosol optical depth in Nouakchott 2000-2013
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2000 | 0.8695 | 0.9052 | 0.896 | 0.70325 | 0.9278 | 0.9865 | 0.78117 | 0.4696 | 0.2405 | 0.3702
2001 | 0.276 | 0.36775 | 0.4088 | 0.7436 | 0.31325 | 0.7084 | 0.7262 | 0.8254 | 0.9795 | 0.5575 | 0.4895 | 0.21075
2002 | 0.3025 | 0.48725 | 0.5454 | 0.337 | 0.52867 | 0.8676 | 0.90075 | 0.7206 | 0.75333 | 0.6165 | 0.4306 | 0.2322
2003 | 0.23383 | 0.4885 | 0.4325 | 0.5725 | 0.83167 | 0.8752 | 0.7845 | 0.905 | 0.7454 | 0.5506 | 0.2888 | 0.3652
2004 | 0.1994 | 0.384 | 0.59217 | 0.552 | 0.43375 | 0.7165 | 0.97133 | 0.655 | 0.6658 | 0.44567 | 0.37525 | 0.30183
2005 | 0.3684 | 0.39267 | 0.2902 | 0.6452 | 0.74633 | 0.61083 | 0.9316 | 0.91825 | 0.72567 | 0.4772 | 0.3386 | 0.4032
2006 | 0.251 | 0.35133 | 0.4844 | 0.77067 | 0.6445 | 0.8135 | 0.91583 | 0.8032 | 0.6875 | 0.59167 | 0.2605 | 0.48975
2007 | 0.49375 | 0.418 | 0.3786 | 0.3885 | 0.68083 | 0.70133 | 0.8174 | 0.90133 | 0.76175 | 0.5162 | 0.3746 | 0.32817
2008 | 0.463 | 0.5065 | 0.5715 | 0.9355 | 0.51467 | 0.6185 | 0.96 | 0.76425 | 0.66533 | 0.603 | 0.3645 | 0.34325
2009 | 0.2694 | 0.337 | 0.5065 | 0.47383 | 0.7228 | 0.68933 | 0.79367 | 0.783 | 1.003 | 0.37417 | 0.25075 | 0.14333
2010 | 0.27333 | 0.2435 | 0.6442 | 0.6066 | 0.764 | 0.67317 | 0.94767 | 0.80283 | 0.6295 | 0.36275 | 0.22325 | 0.26233
2011 | 0.2624 | 0.243 | 0.2772 | 0.64733 | 0.471 | 0.58867 | 0.7044 | 0.6412 | 0.572 | 0.54633 | 0.28467 | 0.308
INTRODUCTION
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
Atmospheric Optical Depth is the coefficient of attenuation of solar radiation by atmosphere, so it’s an indirect measurement of the presence of dust and haze in the atmosphere.
Ref. M. E. Emetere, G.A. Adeyemi “Dataset on aerosol loading and deposition over Nouakchott-Mauritania
Data in brief, 19, 2291-2296 (2018) https://doi.org/10.1016/j.dib.2018.07.018

## Slide 5
Chart: Aerosol loading stagionality in Nouakchott
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2000 | 0.61025 | 0.58977 | 0.59509 | 0.69966 | 0.57663 | 0.54192 | 0.65913 | 0.80217 | 0.86747 | 0.83525 | 0.89151 | 0.89151
2001 | 0.85994 | 0.83598 | 0.82323 | 0.67901 | 0.85098 | 0.69707 | 0.68801 | 0.635 | 0.5461 | 0.76737 | 0.79473 | 0.87301
2002 | 0.85368 | 0.79558 | 0.77245 | 0.84472 | 0.77933 | 0.61133 | 0.59234 | 0.69087 | 0.67391 | 0.74137 | 0.81597 | 0.86909
2003 | 0.86877 | 0.79511 | 0.81533 | 0.76096 | 0.63152 | 0.60701 | 0.65734 | 0.58989 | 0.67807 | 0.77028 | 0.85698 | 0.83673
2004 | 0.87494 | 0.83108 | 0.75234 | 0.76969 | 0.8149 | 0.69296 | 0.55096 | 0.72334 | 0.71814 | 0.81076 | 0.83374 | 0.85384
2005 | 0.83579 | 0.82839 | 0.85665 | 0.72801 | 0.67758 | 0.74395 | 0.5744 | 0.5822 | 0.68828 | 0.79936 | 0.84428 | 0.82504
2006 | 0.86535 | 0.84073 | 0.79666 | 0.66474 | 0.72834 | 0.64156 | 0.5836 | 0.6472 | 0.70752 | 0.75256 | 0.86335 | 0.79463
2007 | 0.7931 | 0.82021 | 0.83273 | 0.82969 | 0.71081 | 0.70063 | 0.63942 | 0.59201 | 0.66948 | 0.78434 | 0.83394 | 0.8471
2008 | 0.80458 | 0.78816 | 0.76139 | 0.57212 | 0.78495 | 0.74045 | 0.55768 | 0.66815 | 0.71837 | 0.7475 | 0.83694 | 0.843
2009 | 0.86142 | 0.84472 | 0.78816 | 0.80061 | 0.68975 | 0.70661 | 0.65239 | 0.65814 | 0.53205 | 0.83407 | 0.8654 | 0.88292
2010 | 0.86054 | 0.86687 | 0.72848 | 0.74587 | 0.66828 | 0.71456 | 0.56497 | 0.6474 | 0.73537 | 0.83745 | 0.87077 | 0.86296
2011 | 0.86294 | 0.86697 | 0.85967 | 0.72699 | 0.80165 | 0.75389 | 0.69909 | 0.72989 | 0.76117 | 0.77207 | 0.85795 | 0.85231
INTRODUCTION
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
Atmospheric Aerosol Loading is the suspensions of solids and/or liquid particles in the air that we breathe, as dust, smoke and haze, measured by the mass concentration of aerosol particles or by an optical measure.
Ref. M. E. Emetere, G.A. Adeyemi “Dataset on aerosol loading and deposition over Nouakchott-Mauritania
Data in brief, 19, 2291-2296 (2018) https://doi.org/10.1016/j.dib.2018.07.018

## Slide 6
INTRODUCTION
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
O2.4-406
Chart: Aerosol optical depth in Nouakchott 2008-2013
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2008 | 0.463 | 0.5065 | 0.5715 | 0.9355 | 0.51467 | 0.6185 | 0.96 | 0.76425 | 0.66533 | 0.603 | 0.3645 | 0.34325
2009 | 0.2694 | 0.337 | 0.5065 | 0.47383 | 0.7228 | 0.68933 | 0.79367 | 0.783 | 1.003 | 0.37417 | 0.25075 | 0.14333
2010 | 0.27333 | 0.2435 | 0.6442 | 0.6066 | 0.764 | 0.67317 | 0.94767 | 0.80283 | 0.6295 | 0.36275 | 0.22325 | 0.26233
2011 | 0.2624 | 0.243 | 0.2772 | 0.64733 | 0.471 | 0.58867 | 0.7044 | 0.6412 | 0.572 | 0.54633 | 0.28467 | 0.308
2012 | 0.3988 | 0.28 | 0.75667 | 0.64967 | 0.74233 | 0.87167 | 0.76267 | 0.60083 | 0.53383 | 0.25 | 0.25875 | 0.188
2013 | 0.5962 | 0.2964 | 0.2044 | 0.4878 | 0.484 | 0.70067 | 0.731 | 0.59717 | 0.4185 | 0.3666 | 0.175

## Slide 7
Chart: Aerosol loading stagionality in Nouakchott 2008-2013
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2008 | 0.80458 | 0.78816 | 0.76139 | 0.57212 | 0.78495 | 0.74045 | 0.55768 | 0.66815 | 0.71837 | 0.7475 | 0.83694 | 0.843
2009 | 0.86142 | 0.84472 | 0.78816 | 0.80061 | 0.68975 | 0.70661 | 0.65239 | 0.65814 | 0.53205 | 0.83407 | 0.8654 | 0.88292
2010 | 0.86054 | 0.86687 | 0.72848 | 0.74587 | 0.66828 | 0.71456 | 0.56497 | 0.6474 | 0.73537 | 0.83745 | 0.87077 | 0.86296
2011 | 0.86294 | 0.86697 | 0.85967 | 0.72699 | 0.80165 | 0.75389 | 0.69909 | 0.72989 | 0.76117 | 0.77207 | 0.85795 | 0.85231
2013 | 0.75054 | 0.85517 | 0.8741 | 0.79537 | 0.79681 | 0.70096 | 0.68554 | 0.75011 | 0.82004 | 0.83632 | 0.87873 | 0.89151
INTRODUCTION
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406

## Slide 8
METHODS
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
Shewhart Control Chart

## Slide 9
METHODS
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
EWMA Control Chart

## Slide 10
METHODS
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
The distribution of Cs-137 is not a normal distribution but it exhibits asymmetry
Density of observations
intervals

## Slide 11
Cs-137 distribution graph (2008-2018) after Box-Cox transformation
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
METHODS
Density of observations
intervals

## Slide 12
RESULTS
Fukushima events
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
Shewhart Control Chart
applied to the measurements of Cs-137 at RN43 (2008-2019)

## Slide 13
RESULTS
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
EWMA Control Chart
applied to the measurements of Cs-137 at RN43 (2008-2019)
Fukushima events

## Slide 14
Statistical study of the Cs-137 detections at RN43 station
M. M. Mounja1, C. Sanguigni2; A. Rizzo2; g. Ottaviano2
1Mauritania National Authority of Radiation, Safety and Nuclear Security (ARSN), Nouakchott, Mauritania
2Italian National Agency for New Technologies, Energy and Sustainable Economic Development (ENEA), Italy]
O2.4-406
CONCLUSION
We have studied some statistical approach to the measuremnt we saw in our IMS radionuclide station located in Nouakchott.
We have also applied process control charts to the dataset and it was clear that the control charts could help to highlight deviation from the normal statistic of the measurements
We have noticed some coincidence with the appearance of Cs-137 and augmented aerosol loading on Noaukchott in spring 2007, 2008 and 2010
New dataset on atmospheric aerosol loading will be searched for
Further studies to investigate correlations will be done in the future, thanks to the collaboration between Mauritania NDC adn Italian NDC